## Slide 1: Entertainment Center Instructions
February 2018

## Slide 2: Features
Smart 4K TV with Cable and Internet access
DVD Blu-ray Player
Wireless & Wired Microphones
CD Players with Karaoke or DJ
External Systems Connect
  Computer Display and Audio
  MP4 Music Player
  Other

## Slide 3: TV and DVD Control
Power On TV
  Press Comcast remote TV button then Power Button
  Comcast box light goes on TV goes on
  If TV fails to go on Press TV remote power button
Power Off TV
  Press Comcast remote TV button then Power Button
  Comcast box light goes off TV goes off
  If TV fails to go off Press TV remote power button
To select TV source: Cable, DVD, Internet use TV remote
  Press menu button to open options at screen bottom
  Use left and right buttons to navigate, go left to Source
  When Sources appear above, press up button on remote
  Use left and right buttons to navigate and pick a Source
  When desired Source is found press center button
  Press down button to get back to options screen at bottom
  Press menu button to close options at screen bottom
TV button
Power
Power
Menu
Center
Up
Dn
L
R
Navigate
Return

## Slide 4: TV Connections
USB 1
USB 2
Audio
Optical
HDMI 1-4 RF Ant
Ethernet
Connect Box
Power

## Slide 5: PA System Instructions
Examine speakers to ensure they are safely attached
Open Credenza doors to ensure equipment does not overheat
Turn on as needed TV & DVD, then PA Power Strip, then Power AMP
Ensure all devices are powered on
Use Power AMP to control ROOM Volume
Left and Right Volume Must Match, turn down to 9 o’clock when done
If needed see detailed settings in the following pages
When done turn off All power including Power AMP
CAUTION DO NOT use microphones closer than 15 feet to speakers
Power AMP
Left
Right
Power

## Slide 6: Microphone Use
SR 40 PRO 2 Microphone 1 & 2 (use these first)
  Slide switch up on mic for on and verify light goes on at receiver
  If light fails to go on or goes on then off replace batteries
  If needed adjust volume on power AMP
  Slide mic switch down for off, verify light goes off at receiver
Audio Technica Mic A (use only if needed & see wired mic)
  Verify Mic A volume is set properly (see detailed instructions)
  Press button at bottom of mic until light goes on at receiver
  If light fails to go on or goes on then off replace batteries
  If needed adjust volume on power AMP
  Press button again to turn off mic, verify light goes off at receiver
Wired Mic
  When not using set its volume to 0 or turn off mic switch on Numark
  If using Mic A then remove wired mic from cabinet & place near users
Turn off MICs when done or batteries will fail
If no sound go to details

## Slide 7: Entertainment Use
TV or DVD (turn on TV, if needed DVD, and then PA)
  Turn down TV speakers to 1, 2, or 3 (too much echo)
  If needed adjust volume on power AMP
CD 1 or 2 (turn on PA)
  On Numark select CD 1 and or 2 switch and press play
  If needed adjust volume on power AMP
  When done switch CH 1 & 2 to Phono / Line so TV & DVD work
External device - computer MP players (turn on PA)
  Find cable quick disconnect near center of hutch
  Find external device cable near center of hutch
  Disconnect cable from DVD and connect external device cable
  If needed adjust volume on power AMP
  When done reconnect DVD player so DVD works
If no sound go to details

## Slide 8: System Configuration
TV
DVD
Quick Disconnect Cable
External 1
Wired Mic
CH2
CH1
Mic
External 2
Speaker L
Speaker R
Wireless Mic A
Wireless Mic 1
Wireless Mic 2
Cables
TV to Numark: RCA-RCA
DVD To Numark: RCA-RCA female link (2) RCA-RCA
External 1: RCA-mini stereo male
External 2: None
Numark to YAMAHA: RCA-RCA RCA-Phone Plug (2)
Wired Mic to Numark: XLR-XLR (1) Y-XLR (1)
Wireless Mic A to Numark: XLR-XLR (1)
Wireless Mic 1 & 2: XLR-XLR (2)
YAMAHA to AMP: XLR-RCA (2)
AMP
YAMAHA
Numark

## Slide 9: Volume Controls
CAUTION - Wired Mic is a source of serious feedback when left in cabinet. Set volume to 0 or switch off or use wired Mic. Yes Wireless Audio Technica Mic A is tied to wired Mic.
Wired Mic
Wireless Audio Technica Mic A
CD1 or
TV
CD2 or
DVD
Master
Center
Mic 1 Mic 2
Wireless
Master
Left
USE AMP TO CONTROL ROOM VOLUME
Right

## Slide 10: Volume Adjustments
TV
  Adjust using Numark CH 1 Slider
  Usually on at 50%
DVD
  Adjust using Numark CH 2 Slider
  Usually on at 50%
Microphone Wired & Audio Technica Wireless
  Adjust using Numark Mic Slider
  Usually off at 0 because of wired mic, on is 50%
Microphones SR 40 PRO 2
  Preset using YAMAHA Mixer Mic Level 1 & 2
  Adjustment not needed

## Slide 11: Room Equalization Settings
System has some frequency equalization abilities
  To deal with room and less than optimal installations
  Current settings must not be changed significantly
Numark Settings:
  Treble +10 Max
  Mid about 1 o’clock
  Bass about 3 o’clock
YAMAHA Settings:
  High +15 DB
  Low about 2 o’clock
Room Echo
  The only way to reduce room echo is to change speaker location

## Slide 12: Power AMP
CH A & B must match: 9 to 11 o’clock
Stereo
Lift
Input
CH A & B from
YAMAHA Mixer
Output
Speakers Polarity
Must Match
USE THIS TO CONTROL ROOM VOLUME
Caution: Do Not bridge. This can damage the speakers with excessive power.

## Slide 13: NUMARK CD Mix 1
Input Mic: Wired & Audio Technical
Input CH 1: TV Cable Box
Input CH 2: DVD or external device
Treble +10 max
Mid 1 o’clock
Bass 3 o’clock
Mic On
Mic: 50%
Output: YAMAHA Mixer
TV
Phono
Ch1: 50%
Fader
Center
DVD
Phono
Ch2: 50%
Adjust so Meters are Full Green
Stereo
Master 60%
1+2
Gain 0
For CD1 or CD2 select using the CH1 or CH2 switch

## Slide 14: NUMARK CD Mix 1
CH1: TV Cable box
CH2: DVD or External Device
Master: YAMAHA Mixer
MIC: Wired & Audio Technica Wireless

## Slide 15
YAMAHA
Mixer
To
Power AMP
From Numark
CD Mix 1
MICs From
SR40 PRO 2
PAD 1 Up
PAD 2 Up
HPF1 Down
HPF2 Down
Red Button
Phantom Up for OFF
Fx1 Down ON
Fx2 Down ON
Mono / Stereo UP
Meter Set -3DB all devices
Start with TV
Master Volume 3 o’clock
Headphones 0
Power on / off
Gain 12 o’clock
High +15 DB o’clock
Low 2 o’clock
Mic Level 1 2 o’clock
Mic Level 2 2 o’clock
Level 3/4 2 o’clock
Level 5/6 0 Not Used
Fx Return Level 11 o’clock
Delay Down, VO. Echo
1/L & 2/R Settings MUST match

## Slide 16: SR 40 PRO 2 Microphone 1 and 2
Level 1 - 12 o’clock
Level 2 - 12 o’clock
Level 1 and 2 settings must match
Goes to YAMAHA Mixer 1/L and 2/R
YAMAHA 1/L
YAMAHA 2/R
Power on/off
MIC has slide switch, Up is on Down is off
If green light does not go on and stay on with MIC on, replace batteries
Turn off MIC when done
On
Mute
Off

## Slide 17: Audio Technica Microphones A and B
Goes to NUMARK CD Mix 1 MIC input
To NUMARK CD Mix 1
MIC has button on bottom, press on press off
If diversity A or B light does not go on and stay on with MIC on, replace batteries
Turn off MIC when done
Push Power

## Slide 18: Audio Technica Microphones A & B

## Slide 19: Speakers

## Slide 20
Sound System Power Turn off when done!