## Slide 1: Entertainment Center Instructions
June 2022

## Slide 2: TV Connections
USB 1
USB 2
Audio
Optical
HDMI 1-4 RF Ant
Ethernet
Connect Box
Power
HDMI 1 Cable
HDMI 2 DVD
HDMI 3 PC

## Slide 3: PA System Instructions
Examine speakers to ensure they are safely attached
Open Credenza doors to ensure equipment does not overheat
Turn on as needed TV & DVD, then PA Power Strip, then Power AMP
Ensure all devices are powered on
Use Power AMP to control ROOM Volume
Left and Right Volume Must Match, turn down to 9 o’clock when done
When done turn off All power including Power AMP
CAUTION DO NOT use microphones closer than 15 feet to speakers
Power AMP
Left
Right
Power

## Slide 4: Wireless Microphone Use
Shure BLX2/PG58
Unscrew Bottom
Press Power Button
Select channel and Group to match Channel and Group on receiver in cabinet
Look at receiver battery light & make sure it is green or replace batteries
Use rechargeable batteries because they only last for 1 or 2 meetings
Turn off MICs when done or batteries will fail

## Slide 5: Wearable Microphone Use
Shure BLX1
Press Power Button at top
Open compartment
Select channel and Group to match Channel and Group on receiver in cabinet
Look at receiver battery light & make sure it is green or replace batteries
Use rechargeable batteries because they only last for 1 or 2 meetings
Turn down volume to stop feedback
Turn off MICs when done or batteries will fail
Volume

## Slide 6: Microphone Use Receiver
Microphones must connect to receiver using the correct Group and Channel
There are 2 receivers, 1 for each Mic
Use Receiver # 2 for the wearable wireless mic
They are always on

## Slide 7: System Configuration
DVD
External 1
Speaker L
Speaker R
Wireless Mic 1
Wireless Mic 2
AMP
YAMAHA
Wired Mics

## Slide 8: Volume Controls
Wireless
Mic 1&2
Master
Left
USE AMP TO CONTROL ROOM VOLUME
Right
DVD
Wired
Mics

## Slide 9: Power AMP
CH A & B must match: 9 to 11 o’clock
Stereo
Lift
Input
CH A & B from
YAMAHA Mixer
Output
Speakers Polarity
Must Match
USE THIS TO CONTROL ROOM VOLUME
Caution: Do Not bridge. This can damage the speakers with excessive power.

## Slide 10
YAMAHA
Mixer
To
Power AMP
From DVD
Wireless
MICs
PAD 1 Up
PAD 2 Up
HPF1 Down
HPF2 Down
Red Button
Phantom Up for OFF
Fx1 Down ON
Fx2 Down ON
Mono / Stereo UP
Meter Set -3DB all devices
Start with TV
Master Volume 3 o’clock
Headphones 0
Power on / off
Gain 12 o’clock
High +15 DB o’clock
Low 2 o’clock
Mic Level 1 2 o’clock
Mic Level 2 2 o’clock
Level 3/4 2 o’clock
Level 5/6 0 Not Used
Fx Return Level 11 o’clock
Delay Down, VO. Echo
1/L & 2/R Settings MUST match

## Slide 11: Speakers

## Slide 12
Sound System Power Turn off when done!